## Slide 1: Karnaugh Maps (K maps)

## Slide 2: What are Karnaugh1 maps?
Karnaugh maps provide an alternative way of simplifying logic circuits.
Instead of using Boolean algebra simplification techniques, you can transfer logic values from a Boolean statement or a truth table into a Karnaugh map.
The arrangement of 0's and 1's within the map helps you to visualise the logic relationships between the variables and leads directly to a simplified Boolean statement.
1Named for the American electrical engineer Maurice Karnaugh.

## Slide 3: Karnaugh maps
Karnaugh maps, or K-maps, are often used to simplify logic problems with 2, 3 or 4 variables.
For the case of 2 variables, we form a map consisting of 22=4 cells
as shown in Figure
A
B
0
1
0
1
Cell = 2n ,where n is a number of variables
00 | 10
01 | 11
A
B
0
1
0
1
A
B
0
1
0
1
Maxterm
Minterm
0
2
1
3

## Slide 4: Karnaugh maps
3 variables Karnaugh map
AB
C
00
01
11
10
0
1
0
2
6
4
5
3
1
7
Cell = 23=8

## Slide 5: Karnaugh maps
4 variables Karnaugh map
AB
CD
00
01
11
10
00
01
11
10
5
3
1
7
6
2
0
4
9
15
13
11
10
14
12
8

## Slide 6: Karnaugh maps
The Karnaugh map is completed by entering a '1‘(or ‘0’) in each of the appropriate cells.
Within the map, adjacent cells containing 1's (or 0’s) are grouped together in twos, fours, or eights.

## Slide 7: Example
2-variable Karnaugh maps are trivial but can be used to introduce
the methods you need to learn. The map for a 2-input OR gate
looks like this:
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A
B
0
1
0
1
1
1
1
B
A
A+B

## Slide 8: Example
A | B | C | Y
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
AB
C
00
01
11
10
0
1
1
1
1
1
1

## Slide 9: Exercise
Let us use Karnaugh map to simplify the follow function.
F1 = m0+m2+m3+m4+m5+m6+m7
F2 = m0+m1+m2+m5+m7
Answer

## Slide 10: Exercise
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Given the truth table, find the simplified SOP and POS form.

## Slide 11: Don’t care term
 |  | X | 
 |  | X | 1
 |  | X | X
 |  | X | X
AB
CD
00
01
11
10
00
01
11
10
AD

## Slide 12: Exercise
Design logic circuit that convert a 4-bits binary code to Excess-3 code
A | B | C | D | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | x | x | x | x
1 | 0 | 1 | 1 | x | x | x | x
1 | 1 | 0 | 0 | x | x | x | x
1 | 1 | 0 | 1 | x | x | x | x
1 1 | 1 1 | 1 1 | 0 1 | x X | X X | X x | X x

## Slide 13
Minterms that may produce either 0 or 1 for the function.
They are marked with an ´ in the K-map.
This happens, for example, when we don’t input certain minterms to the Boolean function.
These don’t-care conditions can be used to provide further simplification of the algebraic expression.
(Example) F = A`B`C`+A`BC` + ABC`
d=A`B`C +A`BC + AB`C
F = A` + BC`
Don’t-care condition
Notes: 13

## Slide 14: Prime Implicants and Covers
An implicant is a product term that can cover minterms of a function.
A prime implicant is a product term that is not covered by another implicant of the function.
An essential prime implicant is a prime implicant that covers at least one minterm that is not covered by any other prime implicant.
A set of implicants is said to be a cover of a function if each minterm of the function is covered by at least one implicant in the set.
A minimal cover is a cover that contains the smallest number of prime implicants and the smallest number of literals..

## Slide 15: illustrating implicants
Minterms: {AB C, A BC, A BC, ABC, ABC}
Groups of two minterms: {A B, AB, A C, BC, BC}
Groups of four minterms: {B}
Prime implicants: {A C, B}
Cover = {A C, B}
MSOP = A C + B

## Slide 16: Algorithm -- Generating and Selecting Prime Implicants
1. Count the number of adjacencies for each minterm on the K-map.
2. Select an uncovered minterm with the fewest number of adjacencies. Make an arbitrary choice if more than one choice is possible.
3. Generate a prime implicant for this minterm and put it in the cover. If this minterm is covered by more than one prime implicant, select the one that covers the most uncovered minterms.
4. Repeat steps 2 and 3 until all minterms have been covered.

## Slide 17
f(A,B,C,D) = m(2,3,4,5,7,8,10,13,15)

## Slide 18: Algorithm -- Generating and Selecting Prime Implicants (Revisited)
1. Circle all prime implicants on the K-map.
2. Identify and select all essential prime implicants for the cover.
3. Select a minimum subset of the remaining prime implicants to complete the cover, that is, to cover those minterms not covered by the essential prime implicants.

## Slide 19
f(A,B,C,D) = m(2,3,4,5,7,8,10,13,15)

## Slide 20: f(A,B,C,D) = m(0,5,7,8,10,12,14,15)

## Slide 21: f(A,B,C,D) = m(1,2,3,6) = AC + BC

## Slide 22: f(A,B,C,D) = BD + BC + BCD

## Slide 23: Function with no essential prime implicants.
f(A,B,C,D) = m(0,4,5,7,8,10,14,15)

## Slide 24: Minimizing a five-variable function. f(A,B,C,D,E) = m(0,2,4,7,10,12,13,18,23,26,28,29)