## Slide 1
School of Mechanical Engineering
Course Code: BME01T1001 Course Name: Engineering Graphics and Introduction to Digital Fabrication
Faculty Name: Mr. Shrikant Vidya Program Name: B.Tech First Year
Projection

## Slide 2
Prerequisite/Recapitulations
Basics of Engineering Graphics
Drawing, Sketching

## Slide 3
Objectives
To acquire knowledge about:
Introduction to Projection
Types of Projection
View comparison
Orthographic Projection
Projection Systems
Projection Symbols

## Slide 4
Introduction to Projection
Any kind of representation of an object on a paper, screen or similar surface by drawing or by photography is called the projection of that object.
Or, when ray of sights (projectors) are drawn from the eyes of the observer and are extended to fall on a plane of projection the object is said to be projected the image obtained is called projection. The size of image depends upon the position of the plane with respect to the object.
PROJECTORS: The imaginary line from block (object) to the plane is called projectors.
PLANE: The flat surface (such as a sheet of paper) is a plane.
PLANE OF PROJECTION: The plane which is used for the purpose of projection is called plane of projection.

## Slide 5
Types of Projection

## Slide 6
View comparison

## Slide 7
Video for Visualization

## Slide 8
Orthographic Projection
When projectors are parallel to each other and perpendicular to the plane is called orthographic projection
Or, Ortho means perpendicular right angles graphics means right angle drawing
a technical drawing in which different views of an object are projected on different reference planes observing perpendicular to respective reference plane

## Slide 9
Orthographic Drawing

## Slide 10
Reference Planes
Horizontal Plane (HP)
Vertical Plane (VP)
Side or Profile Plane (PP)

## Slide 11
Different Views & Notations
– Front View (FV) – Projected on VP – Top View (TV) – Projected on HP – Side View (SV) – Projected on PP

## Slide 12
Projection systems
First angle system
- European countries - ISO standard
2. Third angle system - Canada, USA, Japan, Thailand
( SETUP:-OBSERVER----OBJECT----PLANE OF PROJECTION)
( SETUP:-OBSERVER----PLANE OF PROJECTION----OBJECT)

## Slide 13
First Angle Projection
ROTATION OF PLANES:-
When the projection of an object has been made on the various planes they are brought together on a single sheet of paper by rotating the planes.
The standard practice of rotation of planes is to be keeping the VP fixed & to rotate the HP & PP in clock wise direction away from the object so that they may come in line with VP. The 1st & 3rd quadrant opened out while rotating the plane.
NOTE:-2ND & 4TH quadrant are not used since the FV & TV come(projected)on the same side of xy line & may overlap the view (FV & TV).so 2nd & 4th angles are not used In engineering drawing.

## Slide 14
Third Angle Projection

## Slide 15
First Angle vs. Third Angle Projection
1ST ANGLE OF PROJECTION | 3RD ANGLE OF PROJECTION
The object is kept in the 1st quadrant. The object lies in between the observer & the Plane of projection The plane of projection is assumed to be Non-transparent In this method, when the views are drawn in their relative position, the plan comes below the FV/elevation or the TV drawn below the FV. The left side view is drawn to the right side of the FV. The right side view is drawn to the left side of the FV. This method of projection is used In European Countries & bureau of Indian standard is adopted w.e.f. 1981. | The object is assumed to keep in 3rd quadrant. The plane of projection lies between the observer and the object. The plane of projection is assumed to be transparent In this method, when the views are drawn in their relative position, the plan comes above the elevation or TV is drawn above the FV. The left side view is drawn to the left side of the FV. The right side view is drawn to the right side Of the FV. This method of projection is used In U.S.A & other countries

## Slide 16
Projection Symbols
The front view & side view of a frustum of cone are used to show the symbol for projection method

## Slide 17
Summary
A projection is defined as representation of an object on a two dimensional plane. The following are the elements to be considered while obtaining a projection.
The object
The plane of projection
The point of sight and
The ray of sight
When drawing the orthographic projection the following items should be invariable exist.
The object to be projected.
The projectors
The plane of projection
The observer’s eye or station point
2ND & 4TH quadrant are not used since the FV & TV come(projected)on the same side of xy line & may overlap the view (FV & TV).so 2nd & 4th angles are not used In engineering drawing

## Slide 18
Questions
How do you explain Orthographic Projection?
Why second and fourth angle projections are not used?
Differentiate first and third angle projection on the basis of placement of different views with respect to reference plane

## Slide 19
References
Engineering Drawing by N. D. Bhatt and V. M. Panchal
Engineering Graphics by K. C. John
NPTEL

## Slide 20
Thank You